## Slide 1: 2G/3G/4G Architecture

## Slide 2
UE
MS
Um / Air Interface
Uu / Air Interface
MSC
A
VLR
GMSC
E
G
BSC
BTS
NodeB
Voice (PSTN) Network
RNC
Iub
Abis
SMSC
EIR
HLR
AuC
E
F
SGSN
GGSN
PCRF
OCS/IN
OFCS
Gy
Gx
Gz
Gn
Gd
Gf
Gr
IuPS
Gb
IuCS
Gc
ISP / PDN
CG
Mediation
Ga
C
MME
eNodeB
eNodeB
X2
S-GW
P-GW
HSS
S1 MME
S1-U
S11
S6a
S5/S8
Uu Interface
PCRF
S10
IP NW / ISP / IMS
SGi
Gx
S6d
S3
S4
UE
Radio Network
Core Network
GERAN
UTRAN
EUTRAN
EPC
Gi
S16
PS CORE
CS CORE
S12

## Slide 3: GSM Network Elements
The GSM network architecture is defined in the GSM specifications and it can be grouped into four main areas:
  Mobile station (MS)
  Network and Switching Subsystem (NSS)
  Base-Station Subsystem (BSS)
  Operation and Support Subsystem (OSS)
MS (Mobile Station)
ME (Mobile Equipment) & SIM (Subscriber Identity Module).

## Slide 4
Base Station Subsystem (BSS)
It is also known as radio subsystem, provides and manages radio transmission paths between the mobile station and the Mobile Switching Centre (MSC). BSS also manages interface between the mobile station and all other subsystems of GSM. It consists of two parts:
Base Transceiver Station (BTS):
  It encodes, encrypts, multiplexes, modulates and feeds the RF signal to the antenna.
  It consists of transceiver units.
  It communicates with mobile stations via radio air interface and also communicates with BSC via Abis interface.
Base Station Controller (BSC):
  It manages radio resources for BTS. It assigns frequency and time slots for all mobile stations in its area.
  It handles call set up, transcoding and adaptation functionality handover for each MS radio power control.
  It communicates with MSC via A interface.

## Slide 5
Network Switching Subsystem (NSS)
It consists of following network elements:
Mobile Services Switching Centre (MSC): The main element within the core network area of the overall GSM network architecture is the Mobile switching Services Centre (MSC). The MSC acts like a normal switching node within a PSTN or ISDN, but also provides additional functionality to enable the requirements of a mobile user to be supported. These include registration, authentication, call location, inter-MSC handovers and call routing to a mobile subscriber. It also provides an interface to the PSTN so that the mobile communications calls can be routed from the mobile network to a phone connected to a landline.
Home Location Register (HLR): It is a database that stores and manages user subscriptions. It contains all permanent subscriber information including their service profile, location information and activity status.
Visitor Location Register (VLR): It is a database that contains all temporary subscriber information needed by the MSC to serve visiting subscribers who are temporarily in the area of the MSC. The VLR can be implemented as a separate entity, but it is commonly included as an integral part of the MSC, rather than a separate entity.

## Slide 6
Equipment Identity Register (EIR): The EIR is the entity that decides whether a given mobile equipment will be allowed onto the network or not. The identity of the mobile station is given by the International Mobile Equipment Identity (IMEI). Each time a call is made, the MSC requests the IMEI of the mobile station, which is then send to the EIR for authorization.
Authentication Centre (AuC): It is a function to authenticate each SIM card that attempts to connect to the gsm core network (typically when the phone is powered on). Once the authentication is successful, the HLR is allowed to manage the SIM and services. An encryption key is also generated that is subsequently used to encrypt all wireless communications (voice, SMS, etc.) between the mobile phone and the GSM core network.
Gateway Mobile Switching Centre (GMSC): The Gateway Mobile Switching Centre (GMSC) is a special kind of MSC that is used to route calls outside the mobile network. Whenever a call for a mobile subscriber comes from outside the mobile network, or the subscriber wants to make a call to somebody outside the mobile network the call is routed through the GMSC.

## Slide 7
Short Message Service Center (SMSC): A short message service center (SMSC) is a mobile telecommunication networks element which stores, forwards, converts and delivers SMS messages and maintains unique timestamps in text messages. The main duty of an SMSC is to route SMS messages and regulate the process.
Operation and Support Subsystem (OSS)
The OSS or operation support subsystem is an element within the overall GSM mobile communications network architecture that is connected to components of the NSS and the BSC. It is used to control and monitor the overall GSM network.

## Slide 8: GPRS Network Elements
General packet Radio Service (GPRS) is a packet oriented mobile data service on the 2G and 3G cellular communication system. GPRS is usually attempts to reuse the existing GSM network elements as much as possible. There are new entities called GPRS supports nodes (GSN) which are responsible for delivery and routing of data packets between mobile stations and external packets networks.
There are two types of GSNs:
Serving GPRS Support Node (SGSN)
Gateway GPRS Support Node (GGSN)
There is also a new database called GPRS register which is located with HLR. It stores routing information's and maps the IMSI to a PDN address.

## Slide 9
Base Station Subsystem (Enhancement):
  Each BSC requires the installation of Packet Control Units (PCUs) in addition to software upgrade. They provide physical and logical data interface to BSS to estimate packet data traffic. BTS too require a software upgrade but typically does not involve hardware enhancements.
  When the traffic is originated at the subscriber mobile then it is transported over the air interface to BTS and then from BTS to BSC, the same way in standard GSM call. But at output of BSC the traffic is separated, the voice is sent to the mobile switching center as per standard GSM and the data is sent to the new device called the SGSN via PCU.
GRPS Support Nodes:
  SSGN: The Serving GPRS Support Node is responsible for authentication of GPRS mobiles, registration of mobiles in the network, mobility management, and collecting information for charging for the use of the air interface.
  GGSN: The Gateway GPRS Support Node acts as an interface and a router to external networks. The GGSN contains routing information for GPRS mobiles, which is used to tunnel packets through the IP based internal backbone to the correct Serving GPRS Support Node.

## Slide 10: UMTS Network Elements
The Universal Mobile Telecommunications System (UMTS) is a third-generation mobile cellular system for networks based on the GSM standard.
UMTS system uses the same core network as the GPRS and uses entirely new radio interface. The new radio network in UMTS is called UTRAN (UMTS Terrestrial Radio Access Network) and is connected to the core network (CN) via Iu interface.
The mobile terminal in UMTS is called User Equipment (UE). The UE is connected to Node-B over high speed Uu (up to 2 Mbps) Interface. The Node-B are the equivalent of BTS in GSM and typically serve a cell site. Several Node-Bs are controlled by a single RNCs over the Iub interface. The RNCs are connected to CN through Iu interface. The packet switched data is transmitted through Iu-PS interface and circuit switched data is transferred over Iu-CS interface. One of the new interfaces in UTRAN is Iur interface which connects two RNCs and has no equivalent in GSM system. The Iur interface facilitates handling of RRM (Radio Resource Management) and eliminates the burden from CN.

## Slide 11
UE (User Equipment)
ME (Mobile Equipment) & USIM (UMTS Subscriber Identity Module).
NodeB
NodeB is a term used in UMTS equivalent to the BTS (base transceiver station) used in GSM.
RNC (Radio Network Controller)
RNC is a governing element in the UMTS radio access network (UTRAN) and It’s responsible for controlling the NodeB’s that are connected to it. The RNC carries out radio resource management, some of the mobility management functions and is the point where encryption is done before user data is sent to and from the mobile.

## Slide 12: LTE Network Elements
The high-level network architecture of LTE is comprised of following three main components:
  User Equipment (UE).
  Evolved UMTS Terrestrial Radio Access Network (E-UTRAN).
  Evolved Packet Core (EPC).
The evolved packet core communicates with packet data networks in the outside world such as the internet, private corporate networks or the IP multimedia subsystem.

## Slide 13
User Equipment (UE)
The internal architecture of the user equipment for LTE is identical to the one used by UMTS and GSM which is a Mobile Equipment (ME). The mobile equipment comprised of the following important modules:
  Mobile Termination (MT) : This handles all the communication functions.
  Terminal Equipment (TE) : This terminates the data streams.
  Universal Integrated Circuit Card (UICC) : This is also known as the SIM card for LTE equipment's. It runs an application known as the Universal Subscriber Identity Module (USIM).
  A USIM stores user-specific data very similar to 3G SIM card. This keeps information about the user's phone number, home network identity and security keys etc.

## Slide 14
E-UTRAN (The access network)
The E-UTRAN handles the radio communications between the mobile and the evolved packet core and just has one component, the evolved base stations, called eNodeB or eNB. Each eNB is a base station that controls the mobiles in one or more cells. The base station that is communicating with a mobile is known as its serving eNB.
LTE Mobile communicates with just one base station and one cell at a time and there are following two main functions supported by eNB:
  The eNB sends and receives radio transmissions to all the mobiles using the analogue and digital signal processing functions of the LTE air interface.
  The eNB controls the low-level operation of all its mobiles, by sending them signalling messages such as handover commands.
Each eNB connects with the EPC by means of the S1 interface and it can also be connected to nearby base stations by the X2 interface, which is mainly used for signalling and packet forwarding during handover.

## Slide 15
The Evolved Packet Core (EPC) (The core network)
Below is a brief description of each of the components shown in the above architecture:
Home Subscriber Server (HSS) component has been carried forward from UMTS and GSM and is a central database that contains information about all the network operator's subscribers.
Packet Data Network (PDN) Gateway (P-GW) communicates with the outside world ie. packet data networks PDN, using SGi interface. Each packet data network is identified by an access point name (APN). The PDN gateway has the same role as the GPRS support node (GGSN) and the serving GPRS support node (SGSN) with UMTS and GSM.
Serving gateway (S-GW) acts as a router, and forwards data between the base station and the PDN gateway.

## Slide 16
Mobility management entity (MME) controls the high-level operation of the mobile by means of signalling messages and Home Subscriber Server (HSS).
Policy Control and Charging Rules Function (PCRF) is responsible for policy control decision-making, as well as for controlling the flow-based charging functionalities in the Policy Control Enforcement Function (PCEF), which resides in the P-GW.
The interface between the serving and PDN gateways is known as S5/S8. This has two slightly different implementations, namely S5 if the two devices are in the same network, and S8 if they are in different networks.